## Slide 1: LSA SAF FRP-PIXEL Product (capabilities, validation, applications)
Martin J. Wooster, Weidong Xu,
Gareth Roberts,
and Jiangping He
Background
FRP-PIXEL
Applications
SALGEE2017 workshop Yerevan 18-21 Sep 2017
SEVIRI

## Slide 2: Biomass Burning Atm. CO2 Contribution
Fire CO2 emissions average 2.0 Pg C yr-1
Deforestation & forest degradation is 2nd
largest anthropogenic CO2 source after
fossil fuel combustion.
Together estimated as ~ 15% of net
global annual average CO2 emissions.
Strongest
El Ninos

## Slide 3: Biomass Burning Emissions
Moscow Peat /Forest Fires
during ‘heatwave’ (2010)
Pollution Index Record (June 2013)
Singapore (Feb 2010)
European Heatwave 2007
TOMS Aerosol (SE Asia)
1997 ENSO Fires
Aug 2007 Greek Fires
Munich Re : ~ 56 k additional deaths
Biomass burning a major air pollution source (PM2.5, VOCs, tropospheric O3, CO..).
Respiratory effects.
SE Asia + 200 days/yr-1 > WHO AQ targets.
Notes: Mounting evidence suggests that air pollution contributes to the large global burden of respiratory and allergic diseases including asthma, chronic obstructive pulmonary disease, pneumonia and possibly tuberculosis.
Emissions from landscape fires affect both climate and air quality1. In this study, we combine satellite-derived fire estimates and atmospheric modeling to quantify health effects from fire emissions in Southeast Asia from 1997 to 2006. This region has large interannual variability in fire activity due to coupling between El Niño-induced droughts and anthropogenic land use change2,3. We show that during strong El Niño years, fires contribute up to 200 μg/m3 and 50 ppb in annual average fine particulate matter (PM2.5) and ozone (O3) surface concentrations near fire sources, respectively. This corresponds to a fire contribution of 200 additional days per year that exceed the World Health Organization (WHO) 50 μg/m3 24-hour PM2.5 interim target (IT-2)4 and an estimated 10,800 (6,800–14,300) person (~2%) annual increase in regional adult cardiovascular mortality. Our results indicate that reducing regional deforestation and degradation fires would improve public health along with widely established benefits from reducing carbon emissions, preserving biodiversity, and maintaining ecosystem services.
Munich Re estimated that in all, 56,000 people died from the combined effects of the smog and the heat wave. The 2010 wildfires were the worst on record to that time; in 2012, however, new wildfires broke out, and they proved even more extensive and damaging.[8]
Situation expected to worsen under future climate change

## Slide 4: Operational FRP-PIXEL Product
Delivered operationally to all as part of EUMETSAT Land Surface Analysis Satellite Applications Facility (LSA SAF)
Landsaf.meteo.pt/
KCL developed an online web mapping system for visualizing the near real-time FRP-PIXEL data and the FRP diurnal cycle http://wildfire.geog.kcl.ac.uk/firemap/

## Slide 5: Operational SEVIRI FRP-PIXEL List Product
Delivered operationally to all as part of EUMETSAT Land Surface Analysis Satellite Applications Facility (LSA SAF)
Landsaf.meteo.pt/
>99% process success
15 mins temporal resolution
Product available in 2 hours after overpass
Input to CAMS

## Slide 6: Operational SEVIRI FRP-PIXEL Quality Product
Delivered operationally to all as part of EUMETSAT Land Surface Analysis Satellite Applications Facility (LSA SAF)
Landsaf.meteo.pt/
>99% successful process rate
15 mins temporal resolution
Product available in 2 hours after overpass

## Slide 7: Example Wildfire - July ‘09 Spain
Fire expanded & burned initially exactly matching News reports.
Fire flared again on 23rd July, as illustrated in FRP-PIXEL product.

## Slide 8: SEVIRI - Fire Diurnal Cycle
Fire Diurnal Cycles

## Slide 9: SEVIRI - Fire Diurnal Cycle

## Slide 10: Radiative Transfer of Active Fire Detection

## Slide 11
Planck Function
MIR approach
FRP (MW) corresponds to the ‘radiative strength’ of fire in a pixel, correlating to its rate of fuel combustion and smoke release.
Fire Radiative Power Derivation

## Slide 12
Using MIR radiances, FRP can in theory be estimated to within ~ ±12.5% without knowledge of fire temperature (assuming in range 650 – 1375 K).
Fire Radiative Power Derivation
Fire Effective Temperature (K)
Wooster et al, Remote Sens. Environ (2003)
“Uncertainty” in FRP
Dennison et al. (2006) Remote Sens. Environ, 100.
California Wildfire Temperatures
This temperature range covers vast majority of wildfire temperatures.

## Slide 13: Relationship between Thermal Energy Emitted and Fuel Biomass Burned
Fire Radiative Energy Emitted vs. Fuel Mass Burned
Burnt Biomass
= Energy x CF
Combustion Factor (CF) ~ constant
Time (secs)
Fuel Consumption
Rate (kg.s-1)
Fire Radiative
Power (MW)
Fuel Mass
Burned (kg)
Fire Radiative
Energy (MJ)
FRP (MW)
Mass loss rate (kg/s)
Notes: The left hand graphs show timeseries of fire energy emission rate (called FRP – fire radiative power) and fuel consumption rate. Integrating under the curves gives total Fire Radiative Energy and Total fuel mass burned. This can then be plotted on the rhs scatterplot as one point. Do this for lots of different lab fires of different sized and different fuels – and you find strong linear relationship.
Thus by measuring the energy emitted we can estimate fuel consumption (which is related to the emissions of smoke as stated earlier)

## Slide 14
Seiler, W. and P.J. Crutzen, 1980: Estimates of gross and net fluxes of carbon between the biosphere and the atmosphere from biomass burning. Climatic Change, 2, 207-247
Crutzen, P.J., L.E. Heidt, J.P. Krasnec, W.H. Pollock and W. Seiler, 1979: Biomass burning as a source of atmospheric gases CO, H2 , N2O, NO, CH3Cl and COS. Nature, 282, 253-256.
Emissions of Speciesx (g)
=
Fuel Load Per Unit Area (kg m-2) 
Combustion Completeness (%) 
Emissions Factor (g kg-1)
Biomass Burning Emissions Calculation
Burned Area (m2) 

## Slide 15
Ei = BA x FL x CC x EFi
Ei = FRE x CF x EFi
burnt biomass
sat. obs.
(dynamic) veg. model
Ei = emission of species i [kg(species i)] BA = burnt area [m2]
CC = combustion completeness [kg(burnt fuel) / kg (available fuel)]
EFi = emission factor for species i [kg(species i) / kg(biomass)] FL = fuel load [kg(biomass) / m2]
FRP = fire radiative power [MW] FRE = Fire Radiative Energy [MJ] = ∫ FRP(t) dt
CF = combustion factor [kg(biomass) / MJ (FRE)]
land cover map
believed
~ constant
“key uncertainties” (Reid et al. 2009)
Global Fire Emissions
Database (GFED)
Ei = emission of species i [kg)]
Daily FRP
(single fire)
Geostationary FRE
(Roberts and Wooster, 2008)
Biomass Burning Emissions Calculation
Notes: Possible drop this one?
This shows the eqn normally used for fire smoke emission calculations, vs that used when we take the fire enegery emissinon approach
Top line is burned area x fuel load x combustion completeness (i.e. how much of the available fuel actually burns)
Bottom line is simpler – Fire Radiaitve Enegry x the “Conversion Factor” defined via the lab experiments.
Both are then mutlitpied by the “EF” – the emissions factor that converts burned biomass into an amount of smoke

## Slide 16: Summery
FRP-PIXEL: Operational product on LS ASAF ~10 year;
FRP relate to fuel consumption and smoke release rate;
FRP-PIXEL has genuine full diurnal cycle.

## Slide 17: Global Fires from MODIS
1 km resolution – very sensitive to fires - but ONLY 4 passes per day.
Global database – useful for evaluation of other products.

## Slide 18: Diurnal cycles
Active Fire Pixel Comparison: FRP-PIXEL & MODIS
Error of omission: 67%
Error of commission: 8%

## Slide 19: Fire Pixel “Cluster” FRP Comparison (FRP-PIXEL vs. MODIS )
Slopes: 0.88-0.97
r2: 0.81-0.96
Scatter: 79.9-95.9
RMSD : 87.4-96.1
When SEVIRI and MODIS detect the same fires, the retrieved FRP shows excellent agreement in all four LSA SAF regions.
Conclusion

## Slide 20
When SEVIRI and MODIS observe the same region, the FRP-PIXEL product tends to underestimate total regional-scale FRP, due to missing “small fire” which can be detected by MODIS.
Conclusion
Regional Scale FRP Comparison (FRP-PIXEL vs. MODIS )
Slope = 0.65
R2 = 0.94
1:1

## Slide 21: FRP Frequency Distribution
MODIS: ~10 MW
SEVIRI: ~ 40 MW
“Rollover” Thresholds

## Slide 22: Fire Diurnal Cycle of SEVIRI Active Fire Products
Daily Active Fire Pixel Count
FRP-PIXEL : 89,781
WFABBA : 35,759
FDeM : 13,477
FIR : 14,645
All on 30 Aug 2014
Notes: Global coverage, using Korean COMS for Asian area.

## Slide 23: WFABBA filtered (201408)
False alarm from WFABBA show a random spatial pattern. No abrupt hot area in the map.
FRP-Pixel: Comparison to Alternative SEVIRI Active Fire Products – 21 Aug 2014
Active Fire Pixel Counts
FRP-PIXEL : 1249
WFABBA : 686
FDeM : 346
FIR : 312
FRP-Pixel
WFABBA
FDeM
FIR
All @ 13:15 UTC

## Slide 24: Active Fire Detection Performance : SEVIRI Fire Products vs. MODIS
Chart: SEVIRI Fire Pixel Count
| FRP-PIXEL | ABBA | FDeM | FIR
Total detection | 26113 | 18547 | 8262 | 5661
Omission error (percent) | 77 | 84 | 92 | 95
1 Month Active Fire Error of Omission

## Slide 25: Active Fire Detection Performance : SEVIRI Fire Products vs. MODIS
Chart: SEVIRI fire pixels
| FRP-PIXEL | WFABBA | FDeM | FIR
Total detection | 33414 | 13008 | 7664 | 7151
Confirmed by MODIS | 29037 | 12284 | 7260 | 6730
Commission error (percent) | 13 | 6 | 5 | 6
1 Month Active Fire Error of Commission

## Slide 26: Summery
FRP agree well between MODIS and SEVIRI on ‘per fire’ basis;
FRP-PIXEL is very sensitive detect much more fire than other fires product on SEVIRI;
FRP-PIXEL is the only product give FRP value.

## Slide 27: LSALSA
August 2007 Greek Fires
Fuel Consumption

## Slide 28: August 2007 Greek Fires Aerosol Optical Depth
MODIS - 26th Aug (09:35 UTC)
Modelled Plume AOD
Aerosol Optical Depth (Modelled)
SEVIRI FRP (Observed)
Modeling performed under EU MACC Project
Courtesy by Morcrette, J., Jones, L, Benedetti, A. and Kaiser, J

## Slide 29: Global Fire Assimilation System (GFAS)
Operational deployment of FRP product via EUMETSAT LSA SAF: http://landsaf.meteo.pt/
Combined with MODIS FRP - then used to model fire chemical emissions in Copernicus Atmospheric Service.
https://atmosphere.copernicus.eu/
Modelled CO Biomass Burning Tracer
Observed Global FRP Areal Density

## Slide 30: Carbon Monoxide from Global Biomass Burning
CO Concentration (ppb) @ 700 hPa
NRT CO biomass burning tracer (ppb)
www.gmes-atmosphere.eu/
Notes: Slide shows the concentration of carbon monoxide in the atmosphere that has been emitted by biomass burning (for one day)
You can see major sources of CO over Africa, South America and also a source in North America – which was caused by the huge “Station Fire” that burned in the hills surrounding LA and got close to NASA JPL.
These emissions can be quite rapidly transported thousands of km away from the actual source region – potentially affecting very large areas of the planet and hundreds of millions of citizens etc etc
Europe wants to operationalise information such as this – so we can monitor and forecast the “state of the atmosphere” (e.g. in terms of its concentration of different atmospheric gases and pollutants), in addition to normal weather monitoring and forecasting
Question is – how do we get information on emissions to the atmosphere in real time from all over the world?
Answer is to use observations from remote sensing satellites – but in regions of the electromagnetic spectrum outside those that we see with our eyes. In particular the infrared region.

## Slide 31
Effective fuel-type dependent CF scaled to GFED3.1
CFW: 0.368 g kJ-1
Derivation of conversion factors (CF) from linearly regressing monthly GFED3.1 DM with GFAS1.0 FRE
Kaiser et al. (2012) Biogeosciences

## Slide 32
GFED3.1 Non-Detection Areas 2003-2009
Areas where GFAS1.0 shows Burning but GFED3.1 not
33% of grid cells with GFAS1.0 fire observations not detected by GFED3.1: - typically low fuel consumption (< 2.7 kJ m-2 year-1) - repeated small fires in savanna, deforestation and agricultural areas - contribute < 3% to global FRE
Only 0.1% of grid cells with GFED3.1 fire observations not detected by GFAS1.0
GFAS1.0
GFAS1.0
N monthly fire observations [months]
Frequent Fires in Croplands or Savannah
FRE [kJ m-2 year-1]
SA
DF
EF
AG
Kaiser et al. (2012) Biogeosciences

## Slide 33
Copernicus Atmosphere Monitoring Service
SALGEE Project
Advanced Fire Information System (afis.meraka.org.za)
Operational Applications & Science Initiatives

## Slide 34
Future work: Fire <carbon> Emissions Product
Active Fires & Plume
AOD
Total Particular matter Emissions - Higher spatio-temporal resolution than all other emissions products. Now extending to total carbon emissions.
Based on factors linking FRE directly to atmospheric species.

## Slide 35: Applications
Fuel consumption;
Aerosol optical depth;
Smoke emissions;
Air quality monitoring.