## Slide 1
Atmospheric composition from GOME-2 / METOP measurements
Alessandra Cacciari
and the Atmospheric Composition team at EUMETSAT
Rosemary Munro (lead), Sebastian Gimeno Garcia, Nan Hao, Rasmus Lindstrot, Gabriele Poli, Frank Ruetrich, Bram Sanders, and
Ruediger Lang

## Slide 2: The need for two types of meteorological satellites
Geostationary orbit
Vital for forecasts up to a few hours
Polar orbit
Critical for forecasts up to 10 days

## Slide 3
GEO_AQ_Constellation_Geophysical_Validation_Needs_1.1_2Oct2019.pdf, ceos.org

## Slide 4: Schematic of Remote Sensing Observations
Validation
Sensor
Measurement
Object
Changed Radiation
Radiation
Data Analysis
Final Result
A priori information
Forward Model
What we see
What we already know
What we should see
Courtesy: Andreas Richter -
University of Bremen

## Slide 5: Remote Sensing Observations
Courtesy: Michel Van Roozendael
Royal Belgian Institute for Space

## Slide 6
Atmospheric composition
Stratospheric Ozone & Ozone Depletion Monitoring
Air Quality Monitoring & Forecasting
Biomass Burning
Aerosols and Volcanic Emissions

## Slide 7: EUMETSAT Current and Future Missions for atmospheric composition
Metop current constellation
Metop A 2006 deorbiting planned Nov 2021
Metop B 2012 primary satellite
Metop C 2019 nominal lifetime 2026
GOME-2
Global Ozone Monitoring Experiment
GRAS
GPS Receiver for Atmospheric Sounding
AVHRR
Advanced Very High Resolution Radiometer
HIRS/4
High-resolution Infrared Radiation Sounder
IASI
Infrared Atmospheric Sounding Interferometer
AMSU-A1
Advanced Microwave Sounding Unit-A1
MHS
Microwave Humidity Sounder
ASCAT
Advanced SCATterometer
AMSU-A2
Advanced Microwave Sounding Unit-A2

## Slide 8: The GOME-2 instrument on Metop Measuring atmospheric composition from space
Metop 2006 – present
Item | Specification
Spectral band (nm) | 240‑790
Spectral resolution (nm) | 0.26‑0.51
Spatial resolution (km2) | 80 × 40 (main channels) 80 × 10 (PMD)
Earth coverage (km) | 120‑1920
Spectral channels | 4096 (in four separated optical channels)
Polarization channels | 30 (in two separated optical channels)
Calibration system | Spectral lamp, white lamp, solar diffuser LED
Dimensions | 600 mm × 800 mm × 500 mm
Weight | 68 kg
Main bus voltage | 22‑37 V
Power consumption | 50 W
Data rate interface | 400 kbit

## Slide 9
process, archive, validate and disseminate
Near Real Time Off-line products Data records
products
< 3 hr < 2 weeks after reprocessing activities
https://acsaf.org/
available to
users
O3, NO2, SO2, BrO, HCHO, H2O, OClO columnar content
Ozone profile
AAI
UV indexes
GOME-2 Level2 products

## Slide 10
GOME-2 Level 2 products

## Slide 11: Atmospheric composition measurement Techniques UV/Visible/NIR/SWIR (UVNS) Solar Backscatter
Slide: 11
I0 Spectral
Solar
Irradiance
I Spectral
Radiance
GOME-2 Measurement Concept

## Slide 12: The GOME-2 instrument on Metop Measuring atmospheric composition from space
Courtesy: WDC – DLR
80 × 40 (main channels) 80 × 10 (PMD)
Spectra collected from 240‑790 nm

## Slide 13: The GOME-2 instrument on Metop Measuring atmospheric composition from space
I Spectral
Radiance
I0 Spectral
Solar
Irradiance

## Slide 14: EPS Services and Level 0 data flow

## Slide 15: Data Processing Levels
Data Level | Description
Lev0 | Reconstructed, raw instrument data and payload data at full resolution [BU]
Lev1A | Reconstructed, unprocessed instrument data at full resolution, time-referenced, and annotated with ancillary information, including in-flight calibration coefficients and georeferencing parameters computed and appended but not applied to Level 0 data
Lev1B | Level 1A data processed geolocated and calibrated radiance Eartshine data Solar Spectrum measurements [Wm2sr-1um-1, Wm2um-1]
Lev2 | Retrieved geophysical variables at the same resolution and location as Level 1 source data
Lev3 | Variables mapped on uniform space-time grid scales, usually with some completeness and consistency.

## Slide 16: Data Processing Level and Processing Steps
 | Processing
CALIBRATION Lev0 TO Lev1B | Signals calibration and correction producing measurements independent from the instrument INPUT instrument signal [BU] - scene-dependent corrections polarisation straylight spatial aliasing - detector-dependent corrections spectral calibration (ISRF) radiometric calibration OUTPUT radiance/irradiance [Wm2sr-1um-1, Wm2um-1] Spectral radiance in the UV-VIS-NIR Solar spectra in the UV-VIS-NIR
RETRIEVAL Lev1B TO Lev2 | Retrieval Techniques INPUT radiance/irradiance [Wm2sr-1um-1, Wm2um-1] Full retrieval (OE) Fast retrieval (DOAS, AAI) OUTPUT O3 [DU], NO2 [molec cm-2], HCHO, BrO, SO2
Data Level | Description
Lev0 | Reconstructed, raw instrument data and payload data at full resolution [BU]
Lev1A | Reconstructed, unprocessed instrument data at full resolution, time-referenced, and annotated with ancillary information, including in-flight calibration coefficients and georeferencing parameters computed and appended but not applied to Level 0 data
Lev1B | Level 1A data processed geolocated and calibrated radiance Eartshine data Solar Spectrum measurements [Wm2sr-1um-1, Wm2um-1]
Lev2 | Retrieved geophysical variables at the same resolution and location as Level 1 source data
Lev3 | Variables mapped on uniform space-time grid scales, usually with some completeness and consistency.

## Slide 17: Data Processing Steps CALIBRATION
 | Processing
Lev0 TO Lev1B | Signals calibration and correction producing measurements independent from the instrument INPUT instrument signal + Calib Coeff [BU] On-Ground In-flight - scene-dependent corrections polarisation straylight spatial aliasing - detector-dependent corrections for GOME e.g. dark signal, PPG, etalon, … spectral calibration (ISRF) radiometric calibration geo-referencing OUTPUT radiance, irradiance [Wm2sr-1um-1, Wm2um-1] Spectral radiance in the UV-VIS-NIR Solar spectra in the UV-VIS-NIR
Lev 0 TO Lev1b NRT processing
EUMETSAT Central Ground Segment

## Slide 18: Data Processing Steps RETRIEVAL
 | Processing
Lev1B TO Lev2 | Retrieval Techniques INPUT radiance, irradiance + auxDB [Wm2sr-1um-1, Wm2um-1] RETRIEVAL Full retrieval (OE) Fast retrieval (DOAS, AAI) OUTPUT O3 [DU], NO2 [molec cm-2], HCHO, BrO, SO2

## Slide 19: Data Processing Steps RETRIEVAL
Satellite measurements
Radiation emerged from the interaction with the Atmosphere-Surface system
COMPARED TO
Modelleded measurements
- A priori information on the system (atmospheric scenarios)
- Model of the system (Forward model)

## Slide 20: Data Processing Steps RETRIEVAL
 | Processing
Lev1B TO Lev2 | Retrieval Techniques INPUT radiance, irradiance + auxDB [Wm2sr-1um-1, Wm2um-1] RETRIEVAL Full retrieval (OE) Fast retrieval (DOAS, AAI) OUTPUT O3 [DU], NO2 [molec cm-2], HCHO, BrO, SO2
FULL retrieval
 full detailed FWD model
 time consuming techniques
 error estimates on the retrieved parameters
 Optimal Estimation
 mostly used as reference techniques
FAST retrieval
Simplified methods based on approximations
 assumptions on properties of the atmospheric constituents (spectral extinction, vertical distribution,…)
 fast computational times
 Differential Optical Absorption Spectroscopy,
Absorbing Aerosol Index
mostly used in operational Level2 processing
Lev1b TO Lev2 processing

## Slide 21
Comparison wrt to ground-based measurement in 2nd and 3rd gap
Time series of the % differences to (nrt) ground-based measurements up to 10 April 2020.
Green rectangle: 2nd gap Differences between the two sensors up to 3-4% (January)
Blue rectangle: 3rd gap
Differences between the two sensors up to 2.5 % (December)
GOME2-A and GOME2-B GDP4.8 Level-2 total ozone column (TOC) up to 10 April 2020
Ground-based measurements: Near-real-time TOC data from Brewer and Dobson ground-based stations, collected by the WMO’s Ozone Mapping Centre hosted by LAP/AUTH (available until 16 April 2020).
Courtesy of Laboratory of Atmospheric Physics of Aristotle University of Thesssaloniki

## Slide 22
GOME-2 L2 products
Heue, K. 2018. ‘Two Decades of Homogenized Satellite Ozone Measurements for Climate Services’. In: Deutsche Klima Tagung.
monthly latitudinal mean of the merged data set for the time period between 1995 and 2017
the merged data set is regularly extended
Covering a period of more than 22 years the time series can be used to determine trends,
or look for correlations with other datasets
Total Ozone
The same retrieval algorithm is applied to measurements of from GOME/ERS-2, SCIAMACHY/ENIVSAT, OMI/AURA and
GOME-2/MetOp-A and MetOp-B

## Slide 23
Thank you

## Slide 24: Data Processing Steps CALIBRATION
 | Processing
Lev0 TO Lev1B | Signals calibration and correction producing measurements independent from the instrument INPUT instrument signal + Calib Coeff [BU] On-Ground In-flight - scene-dependent corrections polarisation straylight spatial aliasing - detector-dependent corrections for GOME e.g. dark signal, PPG, etalon, … spectral calibration (ISRF) radiometric calibration geo-referencing OUTPUT radiance, irradiance [Wm2sr-1um-1, Wm2um-1] Spectral radiance in the UV-VIS-NIR Solar spectra in the UV-VIS-NIR
Lev 0 TO Lev1b NRT processing
EUMETSAT Central Ground Segment
Raw data #photons collected at different detector pixels
CALIBRATION
On-ground characterization and calibration
 lab campaign (environmental tests)
 Key data (calibration coefficient)
In-flight calibration
Calibration Unit
measurements with reference sources
(Spectral Light, White Light, Sun)
Update of the Key data wrt to the actual status of the instrument

## Slide 25: Data Processing Steps CALIBRATION
 | Processing
Lev0 TO Lev1B | Signals calibration and correction producing measurements independent from the instrument INPUT instrument signal + Calib Coeff [BU] On-Ground In-flight - scene-dependent corrections polarisation straylight spatial aliasing - detector-dependent corrections for GOME e.g. dark signal, PPG, etalon, … spectral calibration (ISRF) radiometric calibration geo-referencing OUTPUT radiance, irradiance [Wm2sr-1um-1, Wm2um-1] Spectral radiance in the UV-VIS-NIR Solar spectra in the UV-VIS-NIR
Lev 0 TO Lev1b NRT processing
EUMETSAT Central Ground Segment
Photons per pixel  photons per unit wavelength
photons um-1  W m2 sr-1 um-1