## Slide 1: Retrieval and Validation of MODIS and GOES FRP
Wilfrid Schroeder1,2
Louis Giglio1
Ivan Csiszar2
Christopher Justice1
1Department of Geographical Sciences
University of Maryland, College Park
2NOAA/NESDIS Center for Satellite Applications and Research
3rd SALGEE Workshop
March 2013 - Ericeira, Portugal

## Slide 2
On board AM-1 (“Terra”) and PM-1 (“Aqua”) polar orbiters
  Terra 10:30 & 22:30 local overpass
  Aqua 01:30 & 13:30 local overpass
36 spectral bands covering 0.4 to 14.4 µm
  Two 250-m bands
  Five 500-m bands
  Twenty nine 1-km bands
Dedicated 1 km fire bands
  Channel 21: 3.96 µm, ≈ 500 K saturation
  Channel 31: 11.0 µm, ≈ 400 K saturation
Lower noise, lower quantization error, 1-km multipurpose band
  Channel 22: 3.96 µm, ≈ 330 K saturation
Moderate Resolution Imaging Spectroradiometer (MODIS)

## Slide 3: MODIS Data Vocabulary
“Collection”
  Reprocessing round or version
  Currently at Collection 5
  Collection 6 reprocessing later this year
  Swath data arranged as 5-min granules HDF-EOS format
MODIS Tile
  Global sinusoidal grid (10o resolution @ equator)

## Slide 4: MODIS Collection 6 Active Fire Algorithm Refinements
Reduced false alarms in problem areas
Processing extended to oceans and other large water bodies (to detect gas flaring)
Improved cloud mask
Improved detection confidence estimate
Improved land/sea mask*
Improved input data quality*
Use of alternative FRP derivation formula
Collection 5
Collection 6

## Slide 5
Active Fire (Level 2 -- native 5-min swath)
  Fire mask
  QA layer
  Detailed information about each fire pixel
  MOD14 (Terra), MYD14 (Aqua)
Active Fire (Level 3 -- tiled, 10o sinusoidal grid)
  Cumulative fire mask
  Maximum fire radiative power (FRP)
  Daily and 8-day summaries
  MOD14A1 & MOD14A2 (Terra), MYD14A2 & MYD14A1 (Aqua)
Climate Modeling Grid
  Global, 0.5° resolution
  Monthly, 8-day
  MOD14CMH & MOD14C8H (Terra) MYD14CMH & MYD14C8H (Aqua)
Fire Locations
  ASCII
  Monthly
  MCD14ML
MODIS Active Fire Product Formats

## Slide 6
Origins of MODIS Fire Radiative Power
Kaufman et al. 1998
[JGR, 103(D24), 32,215-32,238pp]
Derivation of fire radiative power via simulation of thousands of fire pixel scenarios for MODIS
“… rate of emission of radiative energy and the rate of combustion are proportional to the size of subpixel fire and to the density of the biomass burned in it”
Simplifies traditional
emission estimates:
Biomass load
Combustion factor
Fire area
MODIS ~4 μm channel 21/22 data

## Slide 7
MODIS Fire Radiative Power
Fire pixel
Background
(adjacent pixels)
Up to Collection 5
New with Collection 6
Brightness Temperature
Brightness Temperature
Radiance
Radiance
Pixel Area
Top of Atmosphere

## Slide 8
Geostationary Operational Environmental Satellite Imager
(GOES)
On board East (75oW) and West (135oW) NOAA geostationary satellites
  Western Hemisphere coverage with ≤ 30 min observation frequency
  Rapid Scan Operation (RSO) allowing for higher observation frequency (~5min) during significant events
  Standby unit at 105oW, plus a dedicated Imager over South America
5 spectral bands covering 0.52 to 13.7 µm
  One 1-km band (0.52-0.71 µm)
  Four 4-km bands including 3.73-4.07 µm channel
  Spatial oversampling of ~50% along scan (east-west)
    Most fires will generate two detections
    WF_ABBA (see next slide) will select the brightest of two
Saturation temperature of ~337K in the 4 µm fire channel

## Slide 9
Version 6.5 incorporates spatially explicit fire classification product
  Flagging fire/non-fire pixels including clouds, water, block-out zones (e.g., sun-glint regions)
  FRP retrieval
  Fire size and temperature retrievals
Variable scan sectors and schedules (e.g., full disks, CONUS, etc.)
Active Fire Mask
  McIDAS AREA format (flags fire/non-fire pixels and preserves spatial oversampling)
  Some HDF data
Fire Locations
  ASCII
  Temporally filtered/non-filtered (two coincident detections in less than 12h to avoid false alarms)
  List of individual fire detections and retrievals (size, temp, FRP) + limited metadata
  Removes extra pixels due to GOES Imager spatial oversampling
Additional data available upon request (ASCII format)
  Complete metadata
  Complete list of fire pixels (including extra detections from oversampling)
WF_ABBA v6.5 Active Fire Product

## Slide 10: WF_ABBA Fire Retrievals
Fire Size and Temperature (Dozier)
Fire Radiative Power (FRP)
Fire pixel AND background must be correctly determined
4 & 11 µm
4 µm only
Corrected primarily for atmospheric attenuation (water vapor) and surface emissivity

## Slide 11
Available WF_ABBA Data Sets
GOES West
GOES East
GOES SA (60oW)
METEOSAT
MTSAT-2

## Slide 12
Satellite Fire Data Validation

## Slide 13
Factors Affecting
Fire Detection and Characterization
Fire size
Fire temperature
Biome
Season
Surface temperature
Cloudiness
Types of clouds
Position of sun
Viewing geometry
Characteristics of smoke
Instrument issues
Other

## Slide 14: Satellite Active Fire Validation
Primary Validation: “The process of assessing by independent means the quality of the data products derived from the system outputs” [Justice et al., 2000]
  Use of independent data to directly estimate product uncertainty
  Use of in-situ, airborne or spaceborne reference data sets
    Having more than one coincident reference data set is highly desirable
Ground (point data)
Airborne (<10m)
Spaceborne (10<>100m)
Satellite Product (~1-4km)
Secondary Validation
  Can be used to verify product consistency (e.g., spatial and temporal distribution of fires)
    Example of application includes assessment of product performance immediately after launch when reference data aren’t available
    Ideally, reference data set must be validated
  May complement primary validation

## Slide 15: Reference Data Requirements
Maximum separation between satellite fire and independent reference data must be limited to ~15min
Credit: Csiszar and Schroeder, 2008
Credit: Giglio, 2007
Credit: Schroeder et al, 2008
30 min ahead of MODIS
Coincident with MODIS
±15 min from GOES
±15 min from GOES

## Slide 16
MODIS & GOES Active Fire Detection Validation

## Slide 17: Active Fire Validation (1)
Primary method based on higher resolution Landsat-class imagery. The following data sets were used in support of MODIS and GOES fire validation:
  “Advanced Spaceborne Thermal Emission and Reflection Radiometer”
    Terra only (no Aqua ASTER) – coincident MODIS acquisition
    14 channels
      15 m, 30 m, 90 m
  Landsat Thematic Mapper (TM) and Enhanced Thematic Mapper (ETM+)
    Higher latitude orbit convergence of TM with Terra/MODIS, near-coincident data
    7 channels
      30 m
Always within ≤ 15min from Geostationary data

## Slide 18: Active Fire Validation (2)
Fire mask using Landsat-class imagery
  Sometimes degraded by sensor artifacts (TM-5)
Fire radiative power retrieval using ASTER [Giglio et al., 2008]
  Cannot use simple middle-infrared band approach used with ASTER
  Often degraded by frequent ASTER saturation
Simulated imagery
  Simulating coarse resolution satellite data using ASTER surface temperature, emissivity, and thermal IR input data
Independent burn scar maps
  Burn scars may be associated with false alarms
  Some fires may not leave a scar (piled debris burning in slash/burn sites)
Product intercomparison
  Used to verify consistency among different products (e.g., MODIS x GOES)

## Slide 19
Active Fire Detection Validation
Coincident MOD14 and 30-m ASTER Imagery
Post-Fire Burn Scar Maps
de Klerk (2008)

## Slide 20
Landsat-class
Fire Detection Approach
Use two reflective bands
  One sensitive to emissive radiation from fires
    SWIR band (2.3 m)
  One insensitive to emissive radiation from fires
    NIR band (0.86 m)
  Otherwise highly correlated and sensitive to reflective, non-fire radiation
Approach is reasonable for 30 m pixels, but not applicable to coarser spatial resolution

## Slide 21
Near-nadir pixels
(using coincident ASTER scenes)
Off-nadir pixels
(using near-coincident TM scenes)
MODIS/ASTER 19 Jan 2006 0852UTC (near nadir)
MODIS/TM 04 Aug 2007 1533UTC (52o scan angle)
ASTER
SWIR detector problem after May 2007
Landsat5 TM
Fire-related artifacts – saturation/bleeding
MODIS Active Fire Detection Validation Results

## Slide 22
Near-nadir pixels
(using coincident ASTER scenes)
Off-nadir pixels
(using near-coincident TM scenes)
MODIS/ASTER 19 Jan 2006 0852UTC (near nadir)
MODIS/TM 04 Aug 2007 1533UTC (52o scan angle)
ASTER
SWIR detector problem after May 2007
Landsat5 TM
Fire-related artifacts – saturation/bleeding
MODIS Active Fire Detection Validation Results

## Slide 23: Regional & Global Validation
http://landval.gsfc.nasa.gov/ProductStatus.php?ProductID=MOD14
Biomass burning studies in the Amazon – regional data analyses using a couple hundred reference ASTER & Landsat ETM+ scenes
Comprehensive global validation analyses using ~7,000 ASTER and Landsat TM5 scenes

## Slide 24
Mean FRP
Overall Detection Rate
Fire Pixels Detected per Sample
Temporal Consistency
MODIS Active Fire Detection Validation Results

## Slide 25
MODIS Active Fire Detection Validation Results
Probability of Detection (ASTER/nadir)
Probability of Detection (TM5/off nadir)
Commission Error (TM5/off nadir)
Commission Error (ASTER/nadir)

## Slide 26
MODIS Active Fire Detection Validation Results
MODIS x GOES Detections in the Amazon

## Slide 27
Omission error due to smoke
(confusion w/ clouds)
Examples of pixel misclassification
Commission error (false alarm)

## Slide 28
Commission error (false alarm)
Omission error due to smoke
(confusion w/ clouds)
Examples of pixel misclassification

## Slide 29
Data Simulation &
Product Testing

## Slide 30: Example Simulation Results
MODIS
Temperate deciduous rainforest
Night
0° scan angle
Summer
No background fires

## Slide 31: Example Simulation Results
Observed MODIS/Terra (Ch21)
Simulated (Ch21) using ASTER data to constrain
Data simulation building on higher spatial resolution data sets to re-create fire scenes and test data and algorithm performance

## Slide 32: Example Simulation Results
a  MODIS/Terra (1km)
b, c  VIIRS (750m)
d, e  VIIRS (250x750m)
Background  ASTER (RGB 8-3-1)
a
b
d
c
e

## Slide 33: Other Important Issues: Pixel Spatial Response Characteristics
MODIS/Terra FRP (MW)
A = Nominal pixel area
B = Effective pixel area
Adjusted Values (PSF):
Left pixel = 69.81 MW
Right pixel = 63.03 MW
Point Spread Function (PSF) MODIS
Nominal
1x1 km pixel
Effective
2x1 km pixel
Nominal 1x1km rectangular response

## Slide 34: Potential effects from pixel spatial response characteristics
“true FRP”
“true FRP”
Difference in retrieved FRP due to PSF influence
Difference in retrieved FRP due to PSF influence

## Slide 35
Validation of Satellite Fire Retrievals:
FRP, Size, Temperature

## Slide 36: MODIS x GOES FRP Intercomparison
Inter-comparison of MODIS/Terra FRP with near-coincident GOES Imager data
MODIS = 344MW
GOES = 518MW
MODIS = 360MW
GOES = 509MW
MODIS = 1965MW
GOES = 112MW
Credit: Schroeder et al, 2010
3/4 of points show >20% difference

## Slide 37
Validation of Satellite Fire Retrievals Using Airborne Sensor Data
NASA/Ames AMS
Multispectral
Linescanner
NASA/JPL
MASTER
Multispectral
Linescanner
USFS
FireMapper
Bi-spectral
Focal Plane Array
RIT
WASP
Bi-spectral
Focal Plane Array
MASTER Image of “Day Fire” Los Padres National Forest/CA Sep 19 2006

## Slide 38
Test Case Analysis I
Prescribed Fire at Henry Coe State Park
San Jose, California
18 Oct 2011

## Slide 39: Ground Sampling (actual photos from site)
Fuel load: 30 individual plots
Fire energy: dual-band radiometers (3 sites)
Fire weather: instrumented tower (1 site)

## Slide 40: Pre-Fire Mapping (13 Oct 2011)
Near-coincident Aqua/MODIS acquisition
NASA/Ames AMS image and flight paths on Google Earth
< 3km >
<8km >
13 Oct 2011
21:41UTC
Two flight lines separated by 3km from each other and extending for 8km north-south

## Slide 41: Fire Mapping (18 Oct 2011)
18 Oct 2011
18:12UTC
< 3km >
<10km >
Sequential airborne (NASA/Ames AMS) imaging plus
coincident acquisition with MODIS Terra and Aqua
1 fire pixel detected by MODIS/Terra
Three flight lines separated by 3km from each other and extending for 10km north-south

## Slide 42
Sequential airborne (NASA/Ames AMS) imaging plus
coincident acquisition with MODIS Terra and Aqua
Fire Mapping (18 Oct 2011)
18 Oct 2011
21:24UTC

## Slide 43
Sequential airborne imaging plus
coincident acquisition with MODIS Terra and Aqua
Fire Mapping (18 Oct 2011)
18 Oct 2011
22:25UTC
4 fire pixels detected by MODIS/Aqua

## Slide 44
Airborne Fire Mapping (18 Oct 2011)

## Slide 45
Results: Radiant Heat Flux
Ground
(radiometers)
Airborne
(NASA/AMS)

## Slide 46: Results: Radiant Heat Flux
Minutes
Ground
(radiometers)
Airborne
(NASA/AMS)

## Slide 47
MODIS/Terra:
42.7 MW
AMS:
65.8 MW
~15 seconds apart
MODIS/Aqua:
360 MW
AMS:
458. 8 MW
~20 seconds apart
Results: MODIS Fire Radiative Power

## Slide 48
Results: GOES Fire Radiative Power

## Slide 49
Results: GOES Fire Radiative Power

## Slide 50: Results: Fire Radiative Power
Hours
Airborne
(NASA/AMS)
Spaceborne
(MODIS&GOES)
Airborne data available only for two ~2h segments due to aircraft (NASA/Dryden KingAir) & crew restrictions

## Slide 51
50km

## Slide 52: Emissions Calculations
Biomass burning emissions are calculated using two methods:
  Bottom-up: starts from the ground/fire pixel level calculating the associated emissions using the time-integrated fire metrics (area, energy released) and/or fuel and burning properties (biomass load, burning efficiency, emissions factors)
  Top-down: starts from atmospheric level using particle and/or trace gas concentrations calculating ground fire emissions from clusters of fire pixels
?


?
Fire location&duration
Fire area
(active/burned)
FRP

## Slide 53
In-situ
  Fuel-consumption
  Fuel consistent of entirely grass and was 100% consumed.
  Mean fuel consumption for site 1: 0.225 kg/m2
  Mean fuel consumption for site 2: 0.160 kg/m2
  Energy released
  Radiometer 1: 0.827 MJ/m2
  Radiometer 2: 0.800 MJ/m2
  Radiometer 3: 0.587 MJ/m2
Remote Sensing
  Fuel-consumption factor (FRE-based)
  0.275 kg/MJ
  Total fuel consumed
  (using integrated FRE)
  3.98+06 kg
  Carbon estimates
  (assuming 50% content)
  C = 1.99+06 kg
  CO2 = 7.29+06 kg
  FRE-based OCBC
  (Vermot et al., 2009)
  3.57+04 kg
Preliminary Emissions Results

## Slide 54
Test Case Analysis II:
Use of small/lightweight UAVs in support of fire science applications:
RxCadre Experiment at Eglin Air Force Base,
Niceville,FL Nov/2012
Lead by USDA Forest Service

## Slide 55
Calibration site for airborne IR data
Fixed-wing RC imaging system (VIS-TIR)

## Slide 56
Military-grade small UAV (VIS-TIR)

## Slide 57
Small quad-rotor “scout” (VIS-TIR)

## Slide 58
Data Integration
Coincident data sets are being co-located & reduced allowing for proper characterization of prescribed fire from unique measuring/observation systems
VIIRS 375m Fire Detection Data
Small UAV thermal-IR data
Ground Radiometer Fire Intensity Data

## Slide 59
Conclusions
Major satellite fire products continue to evolve and improve
  Algorithm refinement must be accompanied by data reprocessing
Validation activities have greatly expanded in the last 10 years
  Different studies providing information on algorithm qualities and limitations
Fire retrieval validation and algorithm refinement still requiring attention
  Resources are limited and/or costly
  Community organization is required involving other related disciplines when possible (e.g., atmospheric sciences, fire ecology)
New fire products being developed should take advantage of available techniques and validation data sets
  Landsat-class fire detection products
  Airborne sensors onboard manned/un-manned aircrafts should be more frequently used